## Slide 1: CSE-2204
Computer Architecture and Organization

## Slide 2: Lecture – 1, 2

## Slide 3: Text Books
Computer Architecture and Organization
Hayes J.P., McGraw-Hill.
Computer organization and design: The hardware/software interface
Patterson D.A., Hennessy J.L., Morgan Kaufmann.

## Slide 4: Reference Book
Computer Architecture: A Quantitative Approach
Patterson D.A., Hennessy J.L., Morgan Kaufmann.

## Slide 5: Fixed-Point Arithmetic
Addition
Subtraction
Multiplication
Division

## Slide 6: Half Adder
X0 Y0 | S0 C0
0 0 | 0 0
0 1 | 1 0
1 0 | 1 0
1 1 | 1 1
C0
S0
X0
Y0
S0  X0  Y0 C0  X0Y0

## Slide 7: Full Adder
S0  X0  Y0  C1
C0  X0Y0  X0C1  Y0C1

## Slide 8: Full Adder

## Slide 9: Serial Binary Adder
Least expensive circuit in terms of hardware cost.
It adds the numbers bit by bit and so requires n clock cycle to compute the sum of two n-bit numbers.
Circuit size independent of n.

## Slide 10: Ripple Carry Adder
A 1 appearing on the carry in line of a 1-bit adder cause it to generate a 1 on its carry out line. So, the carry signal propagate through the adder from right to left.
The maximum signal propagation delay is nd, where d is the delay of a full-adder stage.
The amount of hardware increase linearly with n.

## Slide 11: 2’s Complement Adder-Subtracter
When s =0, then X  s = X
When s=1, then X  s = X

## Slide 12: 2’s Complement Adder- Subtracter

## Slide 13: Overflow
When the result of an arithmetic
operation exceeds the
standard word size n, overflow occurs.
Example: let n=8, X=11101011=23510 and Y=00101010=4210 Z = X+Y = 11101011 + 0101010 = 00010101 = 2110
with Cn-1 = C7 = 1.
C7Z = 100010101 = 27710 = 25610 + 2110
The result of an addition simply wraps around when the largest number 2n-1 is exceeds.
For n, the number range for unsigned number is 0 to 2n-1

## Slide 14: Overflow
We can never have overflow on adding a negative and positive number.
Example: let n=8 X=11101011=-2110 and Y=00101010=+4210
Z = X+Y = 00010101 = 2110 and C7 = 1.
So, Cn-1 = 1 does not indicate overflow.
Overflow in 2’s complement addition can result from adding
  two positive numbers or
  two negative numbers.

## Slide 15: Overflow
Case 1: Two numbers are positive.
Let n = 4, 7 + 3 = 0111+0011 = 1010 so, cn-2 = 1
Cn-2 =1 indicates that the magnitude of the sum exceeds the n-1 bits allocated to it.
Case 2: Two numbers are negative.
Let n=4, -7 = 1001, -3 = 1101
so, 1001+1101 = 10110 so, cn-2 = 0
Cn-2 =0 indicates the overflow.

## Slide 16: Overflow
Xn-1 | Yn-1 | Cn-2 | Zn-1 | v
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
Zn 1Zn 2......Z0 : Xn 1 Xn 2......X0  Yn 1Yn 2......Y0
v  Xn 1Yn 1Cn 2  Xn 1Yn 1Cn 2
v  Cn 1  Cn 2

## Slide 17: Carry-Lookahead Adder
It reduce the time required to form carry signals.
It computes the input carry needed b y stage I directly from carrylike signals obtained from all the preceding stages i-1, i-2, ….., 0, rather than waiting for normal carries to ripple slowly from stage to stage.
Adders that use this principle are called carry-lookahead adders.

## Slide 18: Carry-Lookahead Adder
Two signals:
generate signal, gi = xiyi propagate signal, pi = xi + yi
ci = xiyi + xici-1 + yici-1
ci = gi + pici-1
ci-1 = gi-1 + pi-1ci-2
ci = gi + pigi-1 + pipi-1ci-2

## Slide 19: 4-bit Carry-Lookahead Adder

ci = gi + pigi-1 + pipi-1ci-2
c0 = g0 + p0cin
c1 = g1 + p1g0 + p1p0cin
c2 = g2 + p2g1 + p2p1g0 + p2p1p0cin
c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0cin
zi = xi  yi  ci-1 can be written as zi = pi  gi  ci-1

## Slide 20: 4-bit Carry-Lookahead Adder

## Slide 21: 4-bit Carry-Lookahead Adder
Maximum delay is 4d, where d is the average gate delay. It is independent of number of input n.
The number of gates grows in proportion to n2 as n increases.
The complexity of the carry generation logic in the carry lookahead adder, including its gate count, its maximum fan-in, and its maximum fan-out, increase steadily with n.
It limits n to 4.

## Slide 22: Adder Expansion
If we replace n 1-bit adder stages in the n-bit ripple carry adder with n k-bit adders, we obtain an nk-bit adder.
16-bit adder composed of 4-bit adders linked by ripple-carry propagation

## Slide 23: Adder Expansion
If we replace n 1-bit adder stages in the n-bit carry look-ahead adder with n k-bit adders, we obtain an nk-bit adder.
16-bit adder composed of 4-bit adders linked by carry look-ahead

## Slide 24: Complete 2’s Complement Adder-Subtracter

## Slide 25: Complete 2’s Complement Adder-Subtracter

## Slide 26: Carry-Save Adder

## Slide 27: Carry-Save Adder
One of the major speed enhancement techniques used in modern digital circuits is the ability to add numbers with minimal carry propagation.
The basic idea is that three numbers can be reduced to 2, in a 3:2 compressor, by doing the addition while keeping the carries and the sum separate.
10111001
00101010
00111001
Sum: 10101010
Carry: 00111001
Result: 100011100
The sum and carry can then be recombined in a normal addition to form the correct result.