## Slide 1: Lecture - 3

## Slide 2: The Basic Information Types
Instruction
Data
Numbers
Fixed-point
Floating-point Nonnumerical data
Binary
Decimal
Binary
Decimal
Information

## Slide 3: Word Length
Bits | Name | Description
1 | Bit | Logic variable, flag.
8 | Byte | Smallest addressable memory item, Binary-coded decimal digit pair.
16 | Halfword | Short fixed-point number. Short address, Short instruction.
32 | Word | Fixed or floating point number, Memory address, Instruction.
64 | Double word | Long instruction, Double-precision floating point number.
Some Instruction formats of the Motorola 680X0 microprocessor series

## Slide 4: Byte Storage
Byte 3 | Byte 2 | Byte 1 | Byte 0
7 0
Least significant bit
15
31 23
Most significant bit
Indexing convention for the bits and bytes of a word

## Slide 5: Big-Endian Storage Method
Suppose a word Wi is represented as Bi, 3 Bi, 2 Bi, 1 Bi, 0
Most significant byte Bi, 3 of Wi is assigned the lowest address and the least significant byte Bi, 0 is assigned the highest address.
It is so named because it assigns highest address to byte 0 of a word.
Byte 1,0
Byte 1,1
Byte 1,2
Byte 1,3
Byte 0,0
Byte 0,1
Byte 0,2
Byte 0,3
00
01
…001
…000
…002
…003
…004
…005
…006
…007

## Slide 6: Little-Endian Storage Method
Suppose a word Wi is represented as Bi, 0 Bi, 1 Bi, 2 Bi, 3
Most significant byte Bi, 3 of Wi is assigned the highest address and the least significant byte Bi, 0 is assigned the lowest address.
It is so named because it assigns lowest address to byte 0 of a word.
Byte 1,3
Byte 1,2
Byte 1,1
Byte 1,0
Byte 0,3
Byte 0,2
Byte 0,1
Byte 0,0
00
01
…001
…000
…002
…003
…004
…005
…006
…007

## Slide 7: Tags
It is a technique of determining the type of a word.
This is done by associating with each information word a group of bits, called a tag, that identifies the word’s type.
Advantages:
It simplifies instruction specifications.
Tag inspection permits the hardware to check for software errors.
Disadvantages:
They increase memory size.
Add system hardware costs without increasing computing performance.

## Slide 8: Tags
0
51 47
Parity Check bit
Tagged-word format of the B6500/7500 Series
 | Tags | Information Bits
Tag
Interpretation
000
001
010
011
100
101
110
111
Single-precision number Indirect reference word Double-precision number Segment descriptor
Step-index control word Data descriptor Uninitialized operand Instruction

## Slide 9: Error Detection and Correction
The parity bit is appended to an n-bit word X = (xo, xi, … , xn-1) to form the (n+1)-bit word X* = (xo, xi, … , xn-1, c0).
Bit c0 is assigned the value 0 or 1 that makes the number of ones in X* even.
Even Parity:
c0 = xo  xi  …  xn-1
Odd Parity:
c0 = xo  xi  …  xn-1

## Slide 10: Error Detection and Correction
Fig. 3.20 Page 166
Let, B receive the word X = (xo, x i, … , x n-1, c 0).
Then, c*0 = x o  x i  …  x n-1
If, c0 ≠ c*0, the received information contains an error.
If, c0 = c*0, there is no single-bit error.

## Slide 11: Factors to select a number representation
The number types to be represented; for example, integers or real numbers.
The range of values (number magnitudes) likely to be encountered.
The precision of numbers, which refers to the maximum accuracy of the representation.
The cost of the hardware required to store and process the numbers.

## Slide 12: Fixed Point Binary Numbers
The unsigned binary fixed-point format takes the form
bN…b1b0.b-1b-2...bM where each bi is 0 or 1, representing the number ∑bi2i where M<=i<=N.
This is a positional notation in which each digit has a fixed-weight according to it’s position relative to the binary point.
The signed binary number is represented as
xn-1xn-2xn-3…x2x1x0
Sign Magnitude
Using n-bit number format we can represent all integers
N with magnitude |N| in the range 0<= |N| <=2n-1.

## Slide 13: Signed Numbers
3 types of representations of a signed number:
Sign magnitude
+75=01001011
-75=11001011
1’s complement
+75= 01001011
-75 = 10110100
2’s complement
+75= 01001011
-75 = 10110101

## Slide 14: Signed Numbers
Sign magnitude number employ the positional notation for magnitude and simply change the sign bit to represent
+ or -.
In both complement code xn-1 retains the role as sign bit, but remaining bits no longer form a simple positional code when the number is negative.
The advantage of the 2’scomplement code is that subtraction can be performed by logical complementation and addition only. 2’s complement addition and subtraction can be implemented by a simple adder for unsigned numbers.
Multiplication and division are more difficult to implement of 2’s complement code.

## Slide 15: Signed Numbers
Decimal Representation | Sign Magnitude | 1’s Complement | 2’s Complement
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
-0 | 1000 | 1111 | 0000
-1 | 1001 | 1110 | 1111
-2 | 1010 | 1101 | 1110
-3 | 1011 | 1100 | 1101
-4 | 1100 | 1011 | 1100
-5 | 1101 | 1010 | 1011
-6 | 1110 | 1001 | 1010
-7 | 1111 | 1000 | 1001

## Slide 16: Decimal Codes
BCD (Binary coded decimal)
In BCD format each digit di of a decimal number is denoted by a 4-bit equivalent bi,3bi,2bi,1bi,0.
BCD is a weighted (positional) number code where each bi,j has the weight 10i2j.
ASCII
The 8-bit ASCII code represents the 10 decimal digits by a 4-bit BCD field and the remaining 4-bits of the ASCII word have no numerical significance.

## Slide 17: Decimal Codes
Excess-Three Code
The excess-three code can be formed by adding 00112 to the corresponding BCD number.
The advantage of the excess-three code is that it may be processed using the same logic used for binary codes.
Some arithmetic operations are difficult to implement using excess-three code, mainly because it is a non- weighted code.

## Slide 18: Decimal Codes
Excess-Three Code
If two excess-three numbers are added like binary numbers, the required decimal carry is automatically generated from the high-order bits. The sum must be corrected by adding +3.
1000 = 5
+ 1100 = 9
Carry 1 0100
+ 0011
0111 = 4
Binary sum Correction Excess-three sum

## Slide 19: Decimal Codes
Two-out-of-Five
Each decimal digit is represented by a 5-bit sequence containing two 1s and three 0s. There are exactly 10 distinct sequence of this type.
It is single-error detecting code, since changing any one bit results in a sequence that does not correspond to a valid code word.
It uses 5 rather than 4 bits per decimal digit.

## Slide 20: Decimal Codes
Decimal Digit | BCD | ASCII | Excess-three | Two-out-of-five
0 | 0000 | 00110000 | 0011 | 11000
1 | 0001 | 00110001 | 0100 | 00011
2 | 0010 | 00110010 | 0101 | 00101
3 | 0011 | 00110011 | 0110 | 00110
4 | 0100 | 00110101 | 0111 | 01001
5 | 0101 | 00110101 | 1000 | 01010
6 | 0110 | 00110110 | 1001 | 01100
7 | 0111 | 00110111 | 1010 | 10001
8 | 1000 | 00111000 | 1011 | 10010
9 | 1001 | 00111001 | 1100 | 10100

## Slide 21: Decimal Codes
Hexadecimal Numbers:
Uses 16 digits, consisting of decimal digits 0, 1, … , 9 augmented by the six digits A, B, C, D, E and F, which have the numerical values 10, 11, 12, 13, 14 and 15, respectively.
Useful for representing long binary numbers.

## Slide 22: Need for Floating-Point Number
The range of number represented by a fixed-point number is insufficient for many applications, particularly, when very large and very small numbers are required.
Scientific notation allows to represent such numbers using relatively few digits.
For example, it is easier to write 1.0 x 1018 than 1 000 000 000 000 000 000

## Slide 23: Basic Format of Floating-Point Number
Three numbers are associate with a floating-point number: a mantissa M, an exponent E and a base B. The mantissa M is also referred to as the significand or fraction in the literature.
A real number is represented as M × BE.
Example: 1.0 × 1018 where 1.0 = mantissa, 10 = base and
18 = exponent.

## Slide 24: Representation of Floating-Point Number
A floating point number is represented as a word (M,E) consisting of a pair of signed fixed-point numbers: M, which is usually a fraction or integer and E, which is an integer.
Since, B is constant, it is not stored but is simply built into the circuit that process the number.
The number of digits in M determines the precision of (M,E); B and E determines the range.

## Slide 25: Example of Floating-Point Number
Let M and E are both 3-bit, sign magnitude numbers. Then M and E each can assume the values ±0, ±1, ±2, ±3. Let B=2.
All binary words of the form (M, E) = (x00, xxx) represent 0, where x denotes either 0 or 1.
0
+24
+3 +4 +6 +8
+12
+16
-24 -16
-12
-8 -6 -4 -3
+.125
+.25
+.375 +.5 +.75 +1 +1.5 +2
-2 -1.5
-1 -.75
-.5 -.375 -.25 -.125
The real numbers representable by a hypothetical 6-bit, floating-point format

## Slide 26: Floating-Point Number
Smallest nonzero positive number is (001, 111), denoting 1 × 2-3 = 0.125
(101, 111), denoting -1 × 2-3 = -0.125
Smallest nonzero negative number is (111, 111), denoting
-3 × 2-3 = -0.375
Largest positive number is (011, 011), denoting 3 × 23 =
24
Largest negative number is (111, 011), denoting -3 × 2-3 =
-24

## Slide 27: Floating-Point Number
The floating point representation of most real numbers is only approximate. For example, 1.25 is approximated by (011,101) representing 1.5 or by either (001, 000) or (001,
100) representing 1.0.
The result of most calculations with floating point arithmetic only approximate the correct result. For example, the exact result of the addition (011,001) + (011, 010) =18 which is not representable. The closest representative number of 18 is 16 (010, 011).
Include a few extra mantissa digits termed guard digits to reduce approximation errors; the guard digits are removed automatically from the final results.

## Slide 28: Normalization
The same number can be represented in many ways. For example: 1.0 × 1018, 0.1 × 1019, 1000000 × 1012
etc.
It is desirable to have a unique or normal form for each representable number in a floating point system.
A binary number is normalized when it has one non- zero digit to the left of the decimal point.
Example: for IEEE 754 the normalized form 1.M.
An un-normalized number is normalized by shifting the mantissa to the right or left and appropriately incrementing or decrementing the exponent.

## Slide 29: Normalization
Advantages:
It simplifies the exchange of data.
It simplifies the floating point arithmetic algorithm
It increases the accuracy of the numbers that can be stored in a word, since the unnecessary leading 0s are replaced by real digits to the right of the binary point.

## Slide 30: IEEE 754 Floating Point Number
IEEE 754 standard 32-bit floating-point number format
S= 1 bit sign representation
E = 8 bit excess-127. The actual exponent is E-127.
M=23 bit mantissa [ fraction part of sign-magnitude binary significand with hidden bit]
S | E | M
1 8 23

## Slide 31: IEEE 754 Floating Point Number
A real number N = (-1)s2E-127(1.M) where, 0< E<255
N=-1.5 is represented as
1 01111111 10000000000…..0

## Slide 32: IEEE 754 Floating Point Number
A real number N = (-1)s2E-1023(1.M) where,
0< E<2047
S | E | M
1 11 52
IEEE 754 standard 64-bit floating-point number format

## Slide 33: Biasing
If we use 2’s complement or other notation in which negative exponents have 1 in MSB, a negative number will look like a big number. For example, 1.0 × 2-1 is represented as
0 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 ……….
1.0 × 21 is represented as,
0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 ………
It is desirable to represent most negative exponent as 00...000 and most positive as 11….111. This convention is called biased notation.
The exponents are encoded in excess-K code where the exponent field E contains an integer that is the desired exponent value plus
K. The quantity K is called bias and exponent encoded in this way is called a biased exponent.
-1+127=126=01111110 and +1+127=128=10000000

## Slide 34: Biasing
Exponent E | Unsigned value | Bias 127 | Bias 128
111…11 | 255 | +128 | +127
111…10 | 254 | +127 | +126
…………. | ………… | ……… | ………...
100…01 | 129 | +2 | +1
100…00 | 128 | +1 | 0
011…11 | 127 | 0 | -1
011…10 | 126 | -1 | -2
……………. | ……………… | ………. | ………
000…01 | 1 | -126 | -127
000…00 | 0 | -127 | -128
8-bit biased exponent with bias=127 (excess-127) and bias = 128 (excess-128)

## Slide 35: Converting from Decimal to Binary Floating Point
What is the binary representation for the single-precision floating point number that corresponds to X = -12.2510?
What is the normalized binary representation for the number?
-12.2510 = -1100.012 = -1.100012 x 23
What are the sign, stored exponent, and normalized mantissa?
S = 1 (since the number is negative)
E = 3 + 127 = 130 = 128 + 2 = 100000102
M = 100010000000000000000002
X = 110000010100010000000000000000002

## Slide 36: Converting from Decimal to Binary Floating Point
Overflow:
A situation in which a positive exponent becomes too large to fit in the exponent field.
Underflow:
A situation in which a negative exponent becomes too large to fit in the exponent field.