## Slide 1: Lecture – 11

## Slide 2: Booth’s Multiplication Algorithm
It employs both addition and subtraction.
It treats positive and negative operands uniformly.
No special actions are required for negative numbers.
It provides faster execution.

## Slide 3: Booth’s Multiplication Algorithm

## Slide 4: Booth’s Multiplication Algorithm
Step – 1:
Two adjacent bits xixi-1 are examined in each step.
If xixi-1 =01, then Y is added to the current partial product Pi.
If xixi-1 =10, then Y is subtracted from Pi.
If xixi-1 =00 or 11, then neither addition or subtraction is performed.
Step – 2:
Shift the product register right 1 bit.

## Slide 5: Booth’s Multiplication Algorithm
It effectively skips over runs of 1s and runs of 0s that it encounters in X.
It reduces the average number of add-subtract steps and allows faster multipliers to be designed.
It involves more complex circuitry.

## Slide 6: Example
011002 X 001112

## Slide 7: Example
210 X -310 = 00102 X 11012

## Slide 8: Validity of Booth’s Multiplication Algorithm
Let X is a positive integer and contains a subsequence X* consisting of a run of k 1s flanked by two 0s.
In normal multiplication the contribution of X* to P = X × Y is
In booth’s multiplication, xixi-1 =01 which contributes 2iY to P.
When xi-kxi-k-1 = 10 the contribution is -2i-kY to P.
So the net contribution is
If j=m+i-k then we get

## Slide 9: Array Implementation of the Booth Multiplication Algorithm
It requires a multifunction cell capable of addition, subtraction and no operation (skip).
The functions of B are defined by z = a  bH  cH and Cout = (a  D)(b+c) + bc

## Slide 10: Array Implementation of the Booth Multiplication Algorithm
z = a  bH  cH and Cout = (a  D)(b+c) + bc
When HD = 10 the equations reduce to full adder equations.
When HD = 11 the equations reduce to full subtracter equations.
When H = 0 then z = a and carry plays no role in the final result.
A n × n bit multiplier is constructed from n2 + n(n-1)/2 cells.

## Slide 11: Array Implementation of the Booth Multiplication Algorithm
C cell generates control input H and D required by the B cells depending on the combination of xixi-1.
xi | xi-1 | H | D
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 12: Array Implementation of the Booth Multiplication Algorithm

## Slide 13: Floating-Point Addition
9.999 × 101 + 1.610 × 10-1. Assume that we can store four decimal digits of the significand and two decimal digits of the exponent.
Step 1: Align the decimal point of the number that has the smaller exponent.
After shifting, the number is
Step 2: Add the significands.
The sum is

## Slide 14: Floating-Point Addition
Step 3: Normalize the result.
Check for underflow and overflow.
Step 4: Round the result.
Truncate the number if the digit to the right of the desired point is between 0 and 4. Add 1 to the digit if the number to the right is between 5 and 9.

## Slide 15: Floating-Point Addition

## Slide 16: Example of Floating-Point Addition
Add the numbers 0.5 and -0.4375 in binary.

## Slide 17: Example of Floating-Point Addition

## Slide 18: Floating-Point Multiplication
1.110 × 1010 × 9.200 × 10-5. Assume that we can store only four digits of the significand and two digits of the exponent.
Step 1: Calculate the exponent of the product by simply adding the exponents of the operands together.
Using the biased notation,
New exponent = (10+127)+(-5+127) – 127
= 137 + 122 – 127
=132 = 5 + 127
Step 2: Multiply significands.
10.212000ten = 10.212 × 105

## Slide 19: Floating-Point Multiplication
Step 3: Normalize the product and check for underflow and overflow.
Step 4: The number 1.0212 × 106 is rounded to 1.021 × 106.
Step 5: Set the sign the of the product. The sign of the product depends on the sign of the original operands. If they are both the same, the sign is positive. Otherwise it is negative.
So, the product is + 1.021 × 106

## Slide 20: Floating-Point Multiplication

## Slide 21: Example of Floating-Point Addition
Multiply the numbers 0.5 and -0.4375 in binary.
Step 1: -1 + (-2) = -3
Using biased representation,
(-1+127) + (-2+127) – 127 = -3 + 127 = 124
Step 2:
The product is 1.11000 × 2-3 = 1.110 × 2-3

## Slide 22: Example of Floating-Point Multiplication
Step 3: The product is normalized and there is no overflow and underflow.
Step 4: It is already rounded.
Step 5: The signs of the original operands are different. So the sign of the product is negative. So the Final product is
- 1.110 × 2-3
= - 0.21875